## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
Magnets & Magnetism
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. Draw the magnetic field patterns for bar and horseshoe magnets.
2. State the laws of magnetic attraction and repulsion.
3. Describe magnetic lines of force and list their characteristics.
4. Define magnetic flux, and flux density and solve calculations involving these quantities.
5. Explain magnetic induction and its effects.
6. Describe the principles of magnetic screening and its applications.
7. List practical applications for permanent magnets.
L

## Slide 3
What is a magnet?
A solid substance which has the property of attracting to it certain substances which are called Magnetic Substances.
L

## Slide 4
Types of Magnets
Temporary Magnets
Permanent Magnets
* Easily magnetised.
* Loses magnetism when the magnetising force is removed.
* Eg. Soft Iron
* Easily magnetised.
* Retains magnetism when the magnetising force is removed.
* Eg. Hard Iron
A measure of how easily a material can be magnetised is called its Permeability (μ).
L

## Slide 5
Magnetic Materials
Ferromagnetic
Non-magnetic
High Permeability - Usually Ferrous metals
Iron, Steel, Nickel, Cobalt, Ferrites, Alnico & Rare-Earths
Ferrite = Ceramic with metal properties
Alnico = Alloy of Aluminium, Nickel, Cobalt & Copper
Permeability of one (1) - Usually Non-metallic
Air, Plastic, Wood, Water, Paper, Cloth
Rare earths = a group of chemically similar, metallic elements with atomic numbers 57 through to 71.
L

## Slide 6
Magnetic Materials
Paramagnetic
Diamagnetic
Some non-Ferrous metals
Aluminium, Platinum, Manganese, Chromium
Permeability slightly higher than one (1)
Become weakly magnetised in the same direction as the magnetising force.
Other non-Ferrous metals
Gold, Silver, Copper, Zinc
Permeability less than one (1)
Become weakly magnetised in the opposite direction to the magnetising force.
L

## Slide 7
A Compass is an example of a magnet.
The end of a magnet which points NORTH is called the “North Seeking Pole”.
Often shortened to the “North Pole”.
L

## Slide 8
Unlike Poles Attract
N
S
N
S
L

## Slide 9
Like Poles Repel
S
N
N
S
L

## Slide 10
N
S
Magnetic Lines of Force
Called FLUX
L
Notes: Start showing the lines on the OHT with bar and horseshoe magnets.
Use Iron filings and clear OHT Sheets.

## Slide 11
Magnetic Lines of Force
Properties
* Completely closed curves
* Have a definite direction
External from NORTH to SOUTH
Internal from SOUTH to NORTH
* NEVER Cross
* Perfectly Elastic
* Pass unaffected through non-magnetic materials
L

## Slide 12
RN Video Magnetism (Part 3)
Magnetic Fields
L

## Slide 13
Unlike Poles Attract
N
S
N
S
L

## Slide 14
Like Poles Repel
S
N
N
S
L

## Slide 15
Demonstrations
Magnetic Fields
L

## Slide 16
Residual Magnetism
How much magnetism remains when the Magnetizing Force is removed.
Retentivity
A measure of a materials ability to retain a Magnetic Field.
Reluctance
The opposition to the Magnetizing Force.
The higher the RETENTIVITY the higher the RESIDUAL MAGNETISM.
L

## Slide 17
The SI Unit of Magnetic Flux is the Weber (Φ)
Magnetic Flux per unit Area is called Flux Density
The SI Unit of Flux Density is the Tesla (T)
A = Area in m2
1 Wb/m2 = 1 Tesla
1 Wb = 1 x 108 Magnetic Lines of Force
Φ = Flux in Webers
B = Flux Density
L

## Slide 18
Φ = 2 x 10-4 Wb
A1 = 100 mm2
a.
A2 = 400 mm2
b.
Φ = 18 μWb
A1 = 900 mm2
B = ?
B = ?
B = ?
L

## Slide 19
Φair gap= ?
BPoles = ?
Bair gap = 1.7 T
Aair gap = 300 mm2
APole = 220 mm2
L

## Slide 20
Magnetic Keepers
Soft iron bars attached to the pole faces to help retain the magnetic strength of permanent magnets.
L

## Slide 21
Magnetic Screening
Provision of a path of LOW RELUCTANCE to protect apparatus from unwanted or undesirable magnetic influences.
L

## Slide 22
Applications
Motors & Generators
Microphones & Speakers
Radio & Television
Meters & Measuring Instruments
L

## Slide 23
Practical Exercise
Magnets & Magnetism
L