## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
DC Motors
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. State the basic Operating Principle of a Motor.
2. Apply Fleming’s Left Hand Rule for Motors.
3. Describe Back EMF and its affect on Armature Current.
4. Describe Motor Effect and Torque as associated with electric motors.
5. Calculate the values of voltage, Current and Torque associated with DC Motors.
L

## Slide 3
Fleming’s Right Hand Rule (Generators)
In generators we use a force on a conductor in a magnetic field to produce a current.
L

## Slide 4
In motors we use a current in a conductor in a magnetic field to produce a force.
Fleming’s Left Hand Rule (Motors)
Motion
Current
Flux
L

## Slide 5
The DC Motor Converts
Electrical Energy to Mechanical Energy
The action of the DC Motors
and Generators depends on
Mutual or Electromagnetic Induction
The DC Generator Converts
Mechanical Energy to Electrical Energy
L

## Slide 6
S
N
S
N
S
N
(a)
N
S
(b)
N
S
(c)
S
N
(d)
S
N
(e)
N
S
(f)
(g)
(h)
Motion
Current
Flux
L

## Slide 7
F = BIl {N}
The magnitude of the force depends on:
The strength of the magnetic field,
Flux Density (B) {Tesla}
The length of the conductor in the magnetic field,
Length (l) {meters}
The current flowing in the conductor,
Current (I) {Amps}
and
L

## Slide 8
l = 200 mm
B = 0.4 T
I = 30 A
F = BIl
F = 0.4 x 30 x 200 x 10-3
F = 2.4 N
Calculate the force acting on a 200 mm length of conductor carrying 30A of current at right angles to a magnetic field of 0.4 T.
What do we know?
What do we want to know?
L

## Slide 9
N
S
Weakened Magnetic Field
Strengthened Magnetic Field
Rotation
Force
Force
L

## Slide 10
Torque is Turning Effort
and depends on:
T = Fr {Nm}
The Force exerted on the conductor
Radius of the Armature
Force
Radius
Radius
Force
T = BIlr {Nm}
L

## Slide 11
A single loop armature winding of a DC Motor has a diameter of 520mm, a length of 180mm and carries a current of 15A in a magnetic field of 1.1 T. Determine:
The force developed on one half of the loop,
The torque developed on one half of the loop, and
The torque developed by the armature.
l = 180 mm
B = 1.1 T
I = 15 A
F = 1.1 x 15 x 0.180
F = 2.97 N
What do we know?
What do we want to know?
r = 260 mm
d = 520 mm
F = BIl
a.
T½ = 2.97 x 0.260
T½ = 0.7722 Nm
T½ = Fr
b.
T1 = 0.7722 x 2
T1 = 1.544 Nm
T1 = 2T1
c.
The Torque developed on one side of the armature is also developed on the other side so that the total Torque developed on the armature for one turn of a coil is twice that developed on one conductor.
L

## Slide 12
A more practical approach to Torque uses the Motor’s Output and its Rotational Speed.
is the Rotational Speed of the Motor in Radians per Second
L

## Slide 13
Calculate the torque produced by a motor that develops an output of 4.2 kW Output at 1100 rpm.
What do we know?
P = 4.2 kW
n = 1100 rpm
What do we want to know?
L

## Slide 14
When a motor’s armature rotates it has a current induced into it by the generator action.
The generated EMF opposes the Applied Voltage
(iaw Lenz’s Law)
This generated EMF is called the:
Counter, or Back EMF (Eg)
L

## Slide 15
IF
A1
A2
VT
RA
RF
Eg
IL
IA
A1
A2
VT
RF
Eg
IL
RA
IA
A1
A2
VT
RS
Eg
IL
RA
IF
RF
IA
Shunt
Series
Compound
Because the motor is acting as a generator we can use the same models:
Separate
A1
A2
VT
RA
RF
Eg
IA
L

## Slide 16
Eg = kEΦn
Because the motor is acting as a generator we can use the same models, and the same formulae.
BUT now the Applied Voltage (VT) is the larger than the Generated Voltage (Eg).
VT = IARA + Eg
AND the Armature current can be found from:
L

## Slide 17
For a given motor the Torque is proportional to:
Field Flux (Φ),
Armature Current (IA), and
Elements of the machine’s construction which are constant (kT).
So that:
T = kTΦIA
L

## Slide 18
The machine constant for Torque calculations already takes into consideration the Number of Poles (P), the number of conductors (Z) and their paths through the magnetic fields (a).
L

## Slide 19
NOTE:
The machine constant for calculating a generated voltage is NOT THE SAME as the machine constant for calculating Torque.
L

## Slide 20
Automatic Torque Control
As the mechanical LOAD increases
(Load )
Armature Speed (n) decreases
(Speed = n )
Back EMF decreases
(Eg = kEΦn )
Armature Current increases

Motor Torque increases
(T = kTΦIA )
The Armature Speed will adjust itself until there is sufficient Armature Current (IA) to provide the necessary Torque to drive the load, or the machine stops.
L

## Slide 21
IA = 25 A
N = 4 Poles
Φ = 0.016 Wb/Pole
T = 80 x 0.016 x 25
T = 32 Nm
kT = 80
T = kTΦIA
A 4 pole DC Motor has a torque machine constant of 80, carries an armature current of 25 A and operates with a field flux of 0.016 Wb/pole. Determine the torque developed by the motor.
What do we know?
What do we want to know?
Determine the torque developed by this motor if it has a load applied to it such that the armature current increases to 35 A.
IA = 35 A
T = 80 x 0.016 x 35
T = 44.8 Nm
T = kTΦIA
L

## Slide 22
A 650 V seperately excited motor has an effective field flux of 0.08 Wb and operates at a speed of 500 rpm. If the motor has a generation machine constant of 15 and an armature resistance of 0.25 Ω, determine:
The Back EMF,
The Armature current, and
The developed torque.
n = 500 rpm
VT = 650 V
Φ = 0.08 Wb
Eg = 15 x 0.08 x 500
Eg = 600 V
kE = 15
Eg = kEΦn
VT = 650 V
0.25 Ω
RA = 0.25 Ω
What do we know?
IA
A1
A2
RSh
Eg
What do we want to know?
IA = 200 A
L

## Slide 23
Eg = 600 V
IA = 200 A
A 650 V seperately excited motor has an effective field flux of 0.08 Wb and operates at a speed of 500 rpm. If the motor has a generation machine constant of 15 and an armature resistance of 0.25 Ω, determine:
The Back EMF,
The Armature current, and
The developed torque.
n = 500 rpm
VT = 650 V
Φ = 0.08 Wb
kE = 15
VT = 650 V
0.25 Ω
RA = 0.25 Ω
What do we know?
A1
A2
RSh
What do we want to know?
L

## Slide 24
Practical Exercise 9
The DC Motor
L