## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
Inductors & Inductance
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. Describe Self Induction and Inductance.
2. Describe the construction of and draw the Australian Standard symbols for Inductors.
3. Calculate the Inductance of a coil from a number of different characteristics.
4. Identify common types of inductors and list their applications.
5. Describe the construction and uses of Bifilar Windings.
6. Describe the testing procedures for Inductors.
L

## Slide 3
The value of the induced EMF depends on:
The Strength of the Magnetic Field (B),
The length of the conductor, or the Number of turns (N) of the coil, in the Magnetic Field, and
The speed of the conductor (v) in the Magnetic Field.
L

## Slide 4
Faraday’s Law of induction states that:
“… the Induced EMF is proportional to the rate of change of the linkage between the conductors and the magnetic flux. …”
L

## Slide 5
Ex. 1
Determine the flux density of a magnetic field if a conductor 25 mm long cuts through the flux at right angles with a velocity of 15 meters per second to produce a voltage of 6V.
l = 0.025 m
v = 15 ms-1
B = ?? T
e = 6 V
B = e/vl
B = 16 T
B = 6/(15 x 0.025)
What do we know?
What do we want to know?
e = Blv
L

## Slide 6
Ex. 2
N = 150 turns
ΔΦ = (0.3 - 0.1) Wb
e = 150 x 2
e = 300 V
ΔΦ = 0.2 Wb
Δt = 0.1 s
ΔΦ/Δt = 2 Wbs-1
A coil of 150 turns is linked by a flux of 300 mWb. If the flux is reduced to 100 mWb in 100 mS, determine the voltage induced in the coil.
What do we know?
What do we want to know?
L

## Slide 7
N
S
S
N
The expanding field induces an EMF that opposes the applied voltage and hence slows the current’s increase.
+
-
+
-
L

## Slide 8
N
S
N
S
The collapsing field induces an EMF that maintains the applied voltage and hence slows the current’s decay.
-
+
L

## Slide 9
Ex. 3
N = 1000 turns
ΔΦ = (0 - 0.01) Wb
e = 1000 x 0.2
e = 200 V
ΔΦ = - 0.01 Wb
Δt = 0.05 s
ΔΦ/Δt = 0.2 Wbs-1
A coil of 1000 turns carries a current which establishes a flux of 0.01 Wb. If it takes 0.05 seconds for the current to reach its steady state value, determine the self induced emf of the coil.
What do we know?
What do we want to know?
L

## Slide 10
The induced EMF which opposes the change is called:
The EMF of Self Induction
The polarity of this Self Induced EMF is always opposite to the applied voltage so it is often called:
The Back EMF
L

## Slide 11
The property of a coil that opposes changes in current is called:
the Self Inductance (L) of the coil.
or
Inductance (L)
The unit of Inductance is the:
Henry (H)
L

## Slide 12
Inductance is dependent on:
The Rate of change of Flux with respect to change in Current.
and
The Number of Turns of the coil,
L

## Slide 13
The Rate of Change of the Flux is dependent on:
The Number of turns in the coil (N),
and
The Area of the Flux Path (A),
The length of the Flux Path (l).
The permiability of the core (µ),
L

## Slide 14
Then:
Leads to:
L

## Slide 15
Ex. 4
N = 200 turns
l = 200 mm
A = 700 mm2
L = 176 μH
Calculate the inductance of the coil of 200 turns wound on a wooden cylinder 200 mm long and having a cross-sectional area of 700 mm2.
What do we know?
What do we want to know?
Air Core ()
L

## Slide 16
Calculate the inductance of the coil of 200 turns wound on a metal cylinder 200 mm long and having a cross-sectional area of 700 mm2.
L = 462 mH
Ex. 5
N = 200 turns
l = 200 mm
A = 700 mm2
What do we know?
What do we want to know?
Metal Core ()
L

## Slide 17
Symbols
L

## Slide 18
Mutual Inductance
L

## Slide 19
Objectives
At the end of this section students should be able to:
1. Describe what is meant by the term Mutual Inductance.
2. List practical applications of Mutual Inductance.
3. Define and calculate the Time Constant for RL Circuits.
4. Calculate the instantaneous values of Voltages and Currents in an RL Circuit.
L

## Slide 20
Example 1
N = 1500 turns
ΔΦ = 0.01 Wb
Δt = 0.05 s
e = 300 V
A coil of 1500 turns carries a current which establishes a flux of 0.01 Wb. If it takes 0.05 seconds for the current to reach its steady state value, determine the self induced emf of the coil.
What do we know?
What do we want to know?
L

## Slide 21
+
I
A
B
V
If there is a changing magnetic field around one coil then the second coil will have a voltage induced in it by Mutual Inductance.
Show Video RN #9
L

## Slide 22
RL Circuits
R
L
VS
IF
+
-
IB
When current changes the changing magnetic field induces an EMF in the coil that opposes the change and hence slows the current’s change.
Time Constant
T = L/R
+
-
L

## Slide 23
R
L
+
-
Time
VS
T
2T
3T
4T
5T
36.8%
Charge Cycle
T = L/R
VS
I
L

## Slide 24
IMax
R
L
+
Charge Cycle
T = L/R
VS
I
-
Time
T
2T
3T
4T
5T
63.2%
L

## Slide 25
RL Circuits
R
L
VS
IF
+
-
IB
The collapsing field induces an EMF in the coil that assists the applied voltage and hence slows the current’s decay.
T = L/R
-
+
L

## Slide 26
R
L
+
-
Time
VS
T
2T
3T
4T
5T
36.8%
Discharge Cycle
T = L/R
VS
I
L

## Slide 27
IMax
R
L
+
Discharge Cycle
T = L/R
VS
I
-
Time
T
2T
3T
4T
5T
36.8%
L

## Slide 28
For Charge or Discharge
The Inductor Voltage
always starts at a maximum
Voltage always FALLS!!!
L

## Slide 29
For a:
CHARGE – Current Rises
CHARGE – Up
DISCHARGE – Current Falls
DISCHARGE – Down
For a:
L

## Slide 30
Time
100%
T
2T
3T
4T
5T
36.8%
Universal Time Constant Curves (T = RC or T = L/R)
63.2%
L

## Slide 31
2 Ω
0.2 V
+
-
4 H
t = 0 (Switch from Open to Closed)
VL
VR
This is a Series LR Cct, so: IL = IR = IT = 0
and: T = L/R = 4/2 = 2 s
After 5T (5 x 2 = 10s) the magnetic field is established and the current has achieved a steady state. Therefore:
VL = 0 and VR = VS = 0.2 V
IL = IT = IR = V/R = 0.2/2 = 0.1 A = 100 mA
The maximum current will flow in the circuit after t = 5T
@ t = 0 IT = 0 A, VL = 0.2 V, and VR = 0
At t = 0 current begins to flow, and the opposition to current flow is a maximum.
L

## Slide 32
47 Ω
25 V
+
-
0.8 H
Off
On
VL
VR
For the above circuit, calculate:
(a) the circuit time constant,
(b) the circuit steady state current,
(c) the circuit current one time constant after switch ON,
(d) the circuit current one time constant after switch OFF.
L

## Slide 33
If the switch is moved from Off to On @ t = 0:
(A)
T = L/R = 0.8/47 = 17 mS
The steady state is achieved after 5 Time Constants.
(B)
(C)
From the Universal Time Constant Curves @ t = T
47 Ω
25 V
+
-
0.8 H
Off
On
VL
VR
L

## Slide 34
Time
100%
T
2T
3T
4T
5T
Universal Time Constant Curves (T = RC or T = L/R)
63.2%
L

## Slide 35
If the switch is moved from Off to On @ t = 0:
(A)
T = L/R = 0.8/47 = 17 mS
The steady state is achieved after 5 Time Constants.
(B)
(C)
From the Universal Time Constant Curves @ t = T
If the switch is moved from On to Off after the steady state is achieved:
(D)
From the Universal Time Constant Curves @ t = T
47 Ω
25 V
+
-
0.8 H
Off
On
VL
VR
L

## Slide 36
Time
100%
T
2T
3T
4T
5T
36.8%
Universal Time Constant Curves (T = RC or T = L/R)
L

## Slide 37
If the switch is moved from Off to On @ t = 0:
(A)
T = L/R = 0.8/47 = 17 mS
The steady state is achieved after 5 Time Constants.
(B)
(C)
From the Universal Time Constant Curves @ t = T
If the switch is moved from On to Off after the steady state is achieved:
(D)
From the Universal Time Constant Curves @ t = T
47 Ω
25 V
+
-
0.8 H
Off
On
VL
VR
L

## Slide 38
T = L/R
T = 5/10k
T = 500 μs
From the Universal Time Constant Curves at: t = 1 ms = 2T
10 kΩ
10 V
+
-
VL
VR
5 H
Calculate the current flowing in the inductor 1 mS after the initial application of power.
L

## Slide 39
Time
100%
T
2T
3T
4T
5T
86.5%
Universal Time Constant Curves (T = RC or T = L/R)
L

## Slide 40
IMax flows @ t = 5T after the switch is closed, i.e. at:
t = 5T = 5 x 500 μ = 2.5 ms
10 kΩ
10 V
+
-
VL
VR
5 H
T = L/R
T = 5/10k
T = 500 μs
From the Universal Time Constant Curves at: t = 1 ms = 2T
Calculate the current flowing in the inductor 1 mS after the initial application of power.
L

## Slide 41
T = L/R
T = 1.2/1k
T = 1.2 ms
@ t = 0.9 ms = 0.75T
after the switch is closed
From the Universal Time Constant Curves:
1 kΩ
40 V
+
-
VL
VR
1.2 H
Calculate the current flowing in the inductor 0.9 mS and 6 mS after the initial application of power.
L

## Slide 42
Time
100%
T
2T
3T
4T
5T
52.8%
Universal Time Constant Curves (T = RC or T = L/R)
0.75T
L

## Slide 43
T = L/R
T = 1.2/1k
T = 1.2 ms
@ t = 0.9 ms = 0.75T
after the switch is closed
From the Universal Time Constant Curves:
1 kΩ
40 V
+
-
VL
VR
1.2 H
@ t = 6 ms = 5T
after the switch is closed
Calculate the current flowing in the inductor 0.9 mS and 6 mS after the initial application of power.
L

## Slide 44
Time
100%
T
2T
3T
4T
5T
Universal Time Constant Curves (T = RC or T = L/R)
L

## Slide 45
T = L/R
T = 1.2/1k
T = 1.2 ms
@ t = 0.9 ms = 0.75T
after the switch is closed
From the Universal Time Constant Curves:
1 kΩ
40 V
+
-
VL
VR
1.2 H
@ t = 6 ms = 5T
after the switch is closed
Calculate the current flowing in the inductor 0.9 mS and 6 mS after the initial application of power.
L

## Slide 46
Practical Exercise 6
Mutual Inductance
L