## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
The DC Generator Part II
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. Describe and Interpret the No Load Characteristics of a DC Generator.
2. Describe the effects of Armature Reaction.
3. Describe and interpret the Load Characteristics of a Separately Excited DC Generator.
4. Calculate Voltages and Currents in a Separately Excited DC Generator.
L

## Slide 3
Open Circuit Characteristics
A1
A2
Terminal Voltage
RA
Eg
E1
E2
RF
Field Rheostat
DC Supply
Open Circuit – No Load
Separately Excited
Field Windings & Excitation
Armature & Output
L

## Slide 4
Open Circuit Characteristics
Field Current - Amps
Output – Terminal Voltage
Saturation
Speed 1
Speed 2
Same shape and proportions as the B-H Curve
Residual Magnetism giving an EMF for Zero Field Current
L

## Slide 5
VT = Eg = 600 V
Ex. 1
Φ = 0.08 Wb
n = 500 rpm
k = 15
Eg = kΦn
Eg = 15 x 0.08 x 500
Eg = 600 V
Determine the generated and terminal voltages of a separately-excited generator with a machine constant of 15, an effective field flux of 0.08 Wb and an operating speed of 500 rpm.
What do we know?
What do we want to know?
A1
A2
Terminal Voltage
RA
Eg
E1
E2
RF
Field Rheostat
DC Supply
VT = Eg
L

## Slide 6
No current in Armature
No distortion of Magnetic Field
When Armature Current flows
The Magnetic Field is distorted in the direction of rotation
Called Armature Reaction
Generator
L

## Slide 7
Armature Reaction causes:
Sparking at the commutator
Reduced Terminal Voltage
Armature Reaction can be overcome by:
Moving the Brushes
from the central position to the new Neutral Point.
Effective for loads which don’t change much.
L

## Slide 8
L

## Slide 9
Armature Reaction causes:
Sparking at the commutator
Reduced Terminal Voltage
Armature Reaction can be overcome by:
Moving the Brushes
Installing Compensating Windings
Windings in the Field Poles connected in series with the Armature windings.
Most effective and most expensive method.
Used to counteract the Armature Field and shift the Neutral Point back to its central position.
L

## Slide 10
L

## Slide 11
Armature Reaction causes:
Sparking at the commutator
Reduced Terminal Voltage
Armature Reaction can be overcome by:
Moving the Brushes
Intalling Compensating Windings
Windings on the yoke connected in series with the Field Poles.
Most common method.
Installing Interpoles
Used to counteract the Armature Field and shift the Neutral Point back to its central position.
L

## Slide 12
N
S
Separately excited shunt generator with interpoles and compensating windings
Field Windings
L

## Slide 13
Closed Circuit Characteristics
Load Current - Amps
Output – Terminal Voltage
Full Load Voltage
Full Load Current
Open Circuit Voltage
L
Zero Current

## Slide 14
RA
RF
125 Ω
0.25 Ω
A2
A1
E1
E2
Field Rheostat
DC Supply
Eg
Ex. 2
A separately excited generator has a field resistance of 125 Ω and is supplied from a 125 V dc supply. If the generator has an open-circuit terminal voltage of 500 V, an armature circuit resistance of 0.25 Ω and an armature current of 35 A, determine the:
(a) field current
(b) generator terminal voltage
(c) load resistance
What do we know?
What do we want to know?
125 V
35A
RL
IF
VT = 500 - (35 x 0.25) V
VT = eg - IARA
VT = 491.25 V
L
Terminal Voltage
491 V
500 V

## Slide 15
Ex. 3
A separately excited generator has a field resistance of 200 Ω and is supplied from a 250 V dc supply. The armature circuit resistance is 0.2 Ω and the load has a resistance of 10 Ω. Given the generator operates with a field flux of 0.1 Wb, a speed of 1000 rpm and has a machine constant of 5 determine the:
(a) field current
(b) generator terminal voltage
(c) load current
(d) generator terminal voltage when delivering load current
(e) voltage drop across the armature circuit resistance.
What do we know?
What do we want to know?
200 Ω
0.2 Ω
A2
A1
E1
E2
Field Rheostat
250 V
Eg
IL
10 Ω
IF
VT
ΦA = 0.1 Wb
n = 1000 rpm
k = 5
L

## Slide 16
ΦA = 0.1 Wb
IF = 250/200 = 1.25 A
VL = 49.02 x 10 = 490.2 V
Eg = kΦn = 5 x 0.1 x 1000 = 500 V
VA = 49 x 0.2 = 9.8 V
(a)
(b)
(e)
n = 1000 rpm
k = 5
IL = 500/(10 + 0.2) = 49.02 A
(c)
(d)
By KVL: eg = VT + ILRA
IF
A1
A2
E1
E2
VT
0.2 Ω
200 Ω
Eg
250 V
10 Ω
IL
L
VA = 500 – 490.2 = 9.8 V

## Slide 17
Ex. 3
A separately excited generator has a field resistance of 200 Ω and is supplied from a 250 V dc supply. The armature circuit resistance is 0.2 Ω and the load has a resistance of 8 Ω. Given the generator operates with a field flux of 0.098 Wb, a speed of 1000 rpm and has a machine constant of 5 determine the:
(a) field current
(b) generator terminal voltage
(c) load current
(d) generator terminal voltage when delivering load current
(e) voltage drop across the armature circuit resistance.
What do we know?
What do we want to know?
200 Ω
0.2 Ω
A2
A1
E1
E2
Field Rheostat
250 V
Eg
IL
8 Ω
IF
VT
ΦA = 0.098 Wb
n = 1000 rpm
k = 5
L

## Slide 18
ΦA = 0.098 Wb
IF = 250/200 = 1.25 A
VL = 59.76 x 8 = 478.08 V
Eg = kΦn = 5 x 0.098 x 1000 = 490 V
VA = 59.76 x 0.2 = 11.95 V
(a)
(b)
(e)
n = 1000 rpm
k = 5
IL = 490/(8 + 0.2) = 59.76 A
(c)
(d)
By KVL: eg = VT + ILRA
IF
A1
A2
E1
E2
VT
0.2 Ω
200 Ω
Eg
250 V
8 Ω
IL
L
VA = 490 – 478.08 = 11.92 V

## Slide 19
Practical Exercise 7
The Separately
Excited Generator
L