## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
Self Excited Generators
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. Draw the circuit arrangements and connections of various types of Self Excited DC Generators.
2. List the characteristics and applications of Self Excited DC Generators.
3. List and describe the methods of excitation of DC Generators.
4. Describe the methods used to regulate the output voltage of DC Generators.
L

## Slide 3
Types of Self Excited Generators
Series
The field winding is connected in series with the armature.
Shunt
The field winding is connected in parallel, or shunt, with the armature.
Compound
Part of the field windings are connected in shunt with the armature, and part is connected in series
will not work if there is no residual magnetism
field windings must have low resistance
must reach critical speed to generate an EMF
Self excited generators:
L

## Slide 4
E1
E2
Field Rheostat
Field Windings
Shunt Generators
A1
A2
Shunt Field Windings have many turns of small CSA giving HIGH Resistance
L

## Slide 5
E1
E2
Field Rheostat
Field Windings
Shunt Generators
A1
A2
A1
A2
Terminal Voltage
RA
Eg
E1
E2
RF
Shunt Field Windings have many turns of small CSA giving HIGH Resistance
The Field Rheostat is used to control the field flux level and is incorporated with RF for calculations.
L

## Slide 6
Shunt Generator Characteristics
Load Current - Amps
Output – Terminal Voltage
Rated Voltage
Full Load Current
Operation Unstable
L

## Slide 7
Voltage Regulation
Eg. A DC Shunt Generator has an open circuit terminal voltage of 250 V which reduces to 230 V when the generator is providing the rated current. Calculate the Voltage regulation.
Reg % = 8.7 %
L

## Slide 8
Applications of Shunt Generators
Battery Charging
Lighting
Electroplating
Steady loads requiring little regulation
L

## Slide 9
RF
A1
A2
VT
RA
Eg
Eg
POut = 9.6 kW
VT =240 V
RA = 0.05 Ω
RF = 120 Ω
IF = V/R = 240/120 = 2 A
IL = P/V = 9 600/240 = 40 A
IL = P/V
Eg = 240 + (42 x 0.05) V
Eg = VT + IARA
Eg = 242.1 V
IF
Calculate the generated voltage of a 240 V DC shunt generator which has an output of 9.6 kW. The shunt field resistance is 120Ω and the armature resistance is 0.05Ω.
IL
IF = V/R
IA = IL + IF = 40 + 2 = 42 A
IA
IA = IL + IF
L
Eg = 240 + 2.1 V

## Slide 10
Series Generators
A1
A2
E1
E2
Field Rheostat
Field Windings
Compensation Windings are part of the Armature Circuit
Series Field Windings have few turns of large CSA giving LOW Resistance.
L

## Slide 11
Series Generators
A1
A2
E1
E2
Field Rheostat
Field Windings
Compensation Windings are part of the Armature Circuit
Series Field Windings have few turns of large CSA giving LOW Resistance.
The Field Rheostat is used to control the field flux level and is incorporated with RF for calculations.
L
A2
E1
A1
RA
Eg
E2
RF
Terminal Voltage

## Slide 12
Series Generator Characteristics
Load Current - Amps
Output – Terminal Voltage
Rated Voltage
Full Load Current
L

## Slide 13
Applications of Series Generators
Not much used for general applications
Voltage Boosters in long DC Supplies
Experimental Work
L

## Slide 14
IL = P/V = 9 600/240 = 40 A
A1
A2
VT
RF
Eg
RA
VT = 240 V
RF = 0.20 Ω
RA = 0.05 Ω
Eg
POut = 9.6 kW
IL = P/V
Eg = 240 + (40 x 0.25) V
Eg = VT + IA(RA + RF)
Eg = 250 V
Calculate the generated voltage of a 240 V DC series generator which has an output of 9.6 kW. The series field resistance is 0.20Ω and the armature resistance is 0.05Ω.
IA = IL
IL
IA
L
Eg = 240 + 10 V

## Slide 15
Compound Generators
A1
A2
E1
E2
L
Shunt Field Windings have many turns of small CSA giving HIGH Resistance
Series Field Windings have few turns of large CSA giving LOW Resistance.

## Slide 16
Compound Generators
A1
A2
E1
E2
L
Shunt Field Windings have many turns of small CSA giving HIGH Resistance
Series Field Windings have few turns of large CSA giving LOW Resistance.
VT
A1
A2
RF
RS
Eg
RA

## Slide 17
A1
A2
VT
RS
Eg
IL
RA
IF
RF
IA
A1
A2
VT
RS
Eg
IL
RA
IF
RF
IA
Long Shunt
Short Shunt
L

## Slide 18
Compound Generator Characteristics
Load Current - Amps
Output – Terminal Voltage
Rated Voltage
Full Load Current
Level Compounded
Over Compounded
Under Compounded
L

## Slide 19
Applications of Compound Generators
Loads close to the generator
Not often used
Level Compounded
Over Compounded
Under Compounded
Loads some distance from the generator
Shipboard DC Supply
Traction Generators for Locomotives
DC Generators for Aircraft
L

## Slide 20
VT = 240 V
IF = V/R = 240/50 = 4.8 A
IL = P/V = 120 000/240 = 500 A
A1
A2
RF
RS
Eg
RA
Eg
POut = 120 kW
RS = 0.05 Ω
IL = P/V
Eg = 240 + (504.8 x 0.09) V
Eg = VT + IA(RA + RS)
RA = 0.04 Ω
Eg = 285.4 V
Calculate the generated voltage of a 240 V DC compound generator which has an output of 120 kW. The series field resistance is 0.05 Ω, the shunt field resistance is 50 Ω and the armature resistance is 0.04 Ω.
IA = IL + IF
RF = 50 Ω
IF = V/R
IL
IF
IA
IA = IL + IF = 504.8 A
L
Eg = 240 + 45.43 V

## Slide 21
Practical Exercise 8
The Self
Excited Generator
L