## Slide 2
Chapter 11
Magnetism and electromagnets
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 3: About this chapter
Magnetism and electricity are closely related. Most of the electricity we generate relies on this relationship, as do electric motors and many other electrical components.
This chapter:
reviews magnetism, the magnetic field and some of the terms that describe magnetism
looks at the way different types of materials respond to a magnetic field and how they are classified
explains electromagnets and a number of terms and equations related to magnetism.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 4: Contents
11.1 Magnetism
11.2 Magnetic effect of an electric current
11.3 The electromagnet
11.4 Magnetic circuit
11.5 Magnetisation curves
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 5: 11.1 Magnetism
Magnetism is a force created by a magnetic field.
The Earth has a magnetic field that produces the magnetosphere, which protects the Earth from the sun’s solar wind.
A magnet has two poles (north and south pole), so named because a magnet, if allowed to move freely, aligns itself so its north pole points to the Earth’s magnetic North Pole.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 6: Basic compass
The north-seeking pole of a magnet points to the Earth’s magnetic North Pole
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.2

## Slide 7: Magnetic field
A magnetic field is made up of lines of force that travel from the north to the south pole of a magnet
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.3

## Slide 8: Properties of a magnetic field
Properties of a magnetic field include:
they seek the path of least magnetic resistance
in a single bar magnet they attempt to form closed loops
they never cross one another
they all have the same magnetic strength
they become less dense (spread out) in air or other non-magnetic materials, and become more dense when flowing in a magnetic material, such as iron.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 9: Properties of a magnetic field (2)
Properties of a magnetic field include:
parallel lines of force travelling in the same direction repel each other
their density decreases with increasing distance from the poles
they are considered to have direction as if flowing, though no actual movement occurs
they flow externally from a magnet’s north pole to a south pole, internally they flow from the south to the north pole.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 10: Lines of force
Lines of force take the path of least magnetic resistance
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.5

## Slide 11: Magnetic induction
When a magnetic material is in a magnetic field, it becomes temporarily magnetised.
This is called magnetic induction, because magnetism is induced in the material by the magnetic field of the magnet.
The polarity of the induced magnet is the same as if the material itself was a magnet, with lines of force also travelling (externally) from its north to its south pole.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 12: Inducing magnetism
Soft iron can be magnetised by induction by stroking the iron with one or two strong magnets
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.6

## Slide 13: Magnetic materials
Materials are either non-magnetic or magnetic.
Non-magnetic materials have no reaction to or effect on a magnetic field.
All magnetic materials react in some way to a magnetic field and are classified according the type of reaction.
There are three classifications:
ferromagnetic
paramagnetic
diamagnetic.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 14
Ferromagnetic materials
Ferromagnetic materials:
are attracted by a magnetic field, can be magnetised and affect the shape of a magnetic field
have a high permeability (low resistance to lines of force) and are good conductors of a magnetic field
include iron, steel, nickel, cobalt and alloys.
The symbol for permeability is µ (mu)
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 15
Rare earth magnets
Rare earth magnetic alloys can support a stronger magnetic field than conventional alloys. They include:
samarium-cobalt (Sm-Co), an alloy combining samarium, cobalt and iron
neodymium (Nd-Fe-B), an alloy made of neodymium, iron and boron.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 16: Ferrite magnets
Ferrite:
is a ceramic material combining iron oxides in a ceramic base
has similar properties to a ferromagnetic material, except it does not conduct an electric current (insulator)
is classed as a ferrimagnetic material.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 17: Magnets
Examples of ferrite, alnico (alloy of aluminium, nickel and cobalt) and rare earth magnets
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.7

## Slide 18: Paramagnetic materials
Paramagnetic materials:
are weakly attracted to a magnet
include aluminium, platinum, manganese, chromium and oxygen
have a permeability slightly higher than one and become weakly magnetised in the same direction as the magnetising force
have far less strength than a ferromagnetic magnet, and lose magnetism when magnetising force is removed.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 19: Diamagnetic materials
Diamagnetic materials:
also become weakly magnetised, but in the opposite direction to the magnetising force
have a permeability less than one
include Bismuth and carbon graphite, the strongest diamagnetic materials
also include mercury, copper, gold, silver, water, diamonds, wood and living tissue which are less strong.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 20: Non-magnetic materials
Non-magnetic materials:
have a permeability of one
include air, wood, plastic, water, paper and cloth fabrics
are not affected by a magnetic field (don’t become magnetised) and have no effect on the field
for most purposes include paramagnetic and diamagnetic materials which are considered non-magnetic.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 21: Preserving a magnet
A magnet of any type will lose some or all of its magnetism if it’s exposed to a high temperature.
The loss of magnetism is complete at the Curie temperature (for iron ≈ 770 ºC, for neodymium ≈ 300 ºC).
Hammering or jarring a magnet will also affect its magnetic strength.
A magnet can lose its magnetic strength if it’s exposed to another magnetic field.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 22: Magnetic keeper
Magnets should be stored with an iron keeper to preserve their magnetic strength
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.9

## Slide 23: Law of attraction and repulsion
Unlike poles attract, like poles repel
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.8

## Slide 24: Magnetic shielding
A magnetic shield keeps magnetic flux away from an area by providing a high permeability path around the area
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.10

## Slide 25: Magnetic flux
Magnetic flux:
is the total number of lines of magnetic force produced by a magnet
is measured in webers (abbreviated to Wb), where one weber equals 100 million (108) lines of force
is known by the symbol Φ (phi).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 26: Magnetic flux (2)
A typical horseshoe magnet produces a flux of 0.0001 Wb, or 10 000 lines of force.
Expressed with a metrix prefix, 0.0001 Wb becomes 0.1 mWb (milliweber), and for calculations, is written as 0.1 × 10-3 weber.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 27: Flux density
Flux density is flux divided by the area
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.11

## Slide 28: Equation for flux density
where:
B = flux density in teslas (or webers/m2)
Φ = flux in webers
A = area (or csa) in square metres (m2).
One tesla equals one weber per square metre. That is,
one tesla is 108 lines of force in an area of
one square metre (m2).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 29: Applications of permanent magnets
Permanent magnets are used in a range of devices
and tools
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.12

## Slide 30: Summing up
A magnet can be made by exposing a ferromagnetic material to a strong magnetic field.
The process is called magnetic induction, as the magnet is inducing magnetism in the ferromagnetic material.
A magnet has a north and south pole. The north pole of a magnet points towards the Earth’s magnetic North Pole.
Unlike magnetic poles attract; like magnetic poles repel.
A magnetic field (flux) consists of lines of force that flow from the north pole of a magnet to its south pole.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 31: Summing up (2)
Lines do not cross each other, they all have the same magnetic strength and although they have a direction, they don’t actually move.
Materials are classified as ferromagnetic (strongly attracted to a magnetic field), paramagnetic (weakly attracted by a strong magnetic field, e.g. oxygen) and diamagnetic (weakly repelled by a strong magnetic field, e.g. living tissue).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 32: Summing up (3)
A magnet can lose its magnetism as a result of excess heat, physical vibration and stress, and through exposure to a magnetic field of the opposite polarity.
A soft iron keeper across the poles of a magnet helps it retain its magnetism.
Magnetic flux (symbol ) is measured in webers, where one weber (Wb) is 100 million (108) lines of force.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 33: Summing up (4)
Most magnetic fields have a flux in milliwebers (mWb) or microwebers (µWb).
Flux density (B) refers to the number of lines of force () in a given area (A).
B is measured in teslas, where one tesla equals one weber of flux per square metre.
That is:
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 34: 11.2 Magnetic effect of an electric current
An electric current causes a magnetic field to be created around
the conductor
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.13

## Slide 35: Direction of the field
The direction of the magnetic field depends on the direction
of the current
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.14

## Slide 36: Right-hand rule for a conductor
Right-hand thumb (or grip) rule to find the direction of the magnetic field around a conductor
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.15

## Slide 37: Magnetic field around two conductors
When the current is in the same direction, adjacent conductors are attracted to each other
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.16

## Slide 38: Currents in opposite directions
Currents in the opposite direction make adjacent conductors repel each other
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.17

## Slide 39: Force between two conductors
where:
F = force in newtons (N) per metre length
I1 = current in one conductor
I2 = current in the other conductor
d = distance in metres between the conductors.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 40: 11.3 The electromagnet
The magnetic field around a coil of wire is the same as a
permanent magnet
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.19

## Slide 41: Right-hand rule for a coil
Use the right-hand rule to find the north pole of an electromagnet
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.20

## Slide 42: Magnetomotive force
The strength of the magnetic field produced by an air-cored electromagnet depends on the coil current and number of turns.
The product of these two values is called magnetomotive force (Fm).
That is: Fm = I × N
where:
Fm = magnetomotive force in ampere-turns (At)
I = current in amperes
N = number of turns.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 43: Magnetomotive force examples
Magnetic flux produced by an electromagnet is proportional to the current and the number of turns
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.21

## Slide 44: Magnetising force
Magnetising force depends on the ampere turns of the coil and the length of the magnetic circuit
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.22

## Slide 45: Magnetising force equation
Magnetising force (H) is magnetomotive force divided by length.
That is:
where:
H = magnetising force in ampere-turns per metre (At/m)
Fm (NI) = magnetomotive force in ampere-turns (At)
l = length of magnetic path in metres (m).
or
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 46: Magnetising force examples
Magnetising force is the same in all parts of an iron core and is inversely proportional to the length of the core
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.23

## Slide 47: Summing up
Magnetomotive force is the force that establishes and maintains a magnetic flux in a magnetic circuit. Symbol is Fm, measured in ampere-turns (At).
Magnetising force is magnetomotive force per unit length. For air-cored solenoid, the length is that of the coil, for iron-cored solenoid it’s the average length of the iron core. Symbol is H, unit is ampere-turns per metre (At/m).
Magnetic flux is the total number of lines an electromagnet or a permanent magnet produces.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 48: Summing up (2)
Flux density is the number of lines per square metre. Symbol is B, unit is the tesla (T).
The right-hand thumb rule can be used to find the north pole of an electromagnet.
Adjacent current-carrying conductors will have a force acting to repel them (currents in different directions) or attract them (current in the same direction).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 49: 11.4 Magnetic circuit
The magnetic circuit:
is like an electric circuit, where voltage causes current to flow, which is opposed by the resistance of the circuit
has magnetomotive force (Fm) equivalent to voltage, and magnetic flux (Φ) equivalent to current
is the path taken by the flux, so its ability to conduct the flux is important. This is related to the material’s permeability.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 50: Relative permeability (µr)
This compares the permeability of a material to the permeability of air (or vacuum).
Symbol is µr (does not have a measurement unit)
where:
B = flux density in teslas (or webers/m2).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 51: Permeability of air (µ0)
In air (or a vacuum), the ratio of flux density (B) and magnetising force (H) producing the flux gives a value called the permeability of air (free space).
This value is constant regardless of the magnetising force, and is called µ0.
µ0 = 4 x 10–7 (exactly) or for practical purposes, 1.26 × 10–6 henry/metre (H/m).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 52: Absolute permeability (µ)
The absolute permeability (µ) of a material is calculated
by multiplying its relative permeability by the
permeability of air.
That is:
 = r  0
Note: Absolute permeability (µ) is sometimes referred to as permeability.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 53: Permeability in terms of B and H
Absolute permeability of a material can also be calculated with:
where:
B is the flux density (tesla)
H is the magnetising force (At/m).
This equation can be transposed in terms of either B or H, giving:
and
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 54: Permeability comparison
Relative permeability (µr) changes with flux density (B). The values shown give an approximate range. Minimum values of permeability (µ) are given.
Notes: 31 Jul 2026
Install HV equipment
<number>
Table 11.1 from page 237

## Slide 55: Reluctance
A magnetic path has resistance to magnetic flux, referred to as its reluctance.
The symbol for reluctance is Rm
Measurement unit is the ampere-turn per weber (At/Wb).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 56: Rm in terms of Ohm’s law
In an electric circuit, Ohm’s law relates V, I and R. In a magnetic circuit, there’s a similar relationship between magnetomotive force Fm, magnetic flux  and
reluctance Rm:
where:
 is flux in webers (Wb)
Fm is magnetomotive force in ampere-turns (At)
Rm is reluctance in ampere-turns per weber (At/Wb).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 57: Factors affecting rm
The reluctance of a magnetic circuit depends on:
length – the longer the magnetic circuit, the higher the reluctance
cross-sectional area – the smaller the csa, the higher the reluctance
permeability – the lower the permeability, the higher the reluctance.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 58: Rm in terms of µ and area
Reluctance of a magnetic circuit can be calculated with:
where:
Rm is reluctance in ampere-turns per weber (At/Wb)
µ0 is permeability of air = 1.26 × 10–6 henry/metre
µr is relative permeability (if known)
µ is absolute permeability (if known)
A is the cross-sectional area in square metres (m2).
or
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 59: Effect of air gap on reluctance
A relay has an air-gap in the magnetic path when the armature is open, which increases the reluctance of the magnetic circuit
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.25

## Slide 60: Summing up
Absolute permeability or permeability (µ) is the ability of a material to conduct magnetic flux; unit is henrys per metre
Permeability of a vacuum (µ0) is a constant and equals approximately 1.26 × 10–6 henrys per metre (H/m).
Relative permeability (symbol µr) is a measure of the increase in flux density a magnetic material causes compared to air, for the same magnetising force. For ferromagnetic materials, µr is always greater than one.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 61: Summing up (2)
Permeability (µ) of a material is the product of its relative permeability (µr) and µ0.
It also equals flux density (B) divided by the magnetising force (H). That is:
Reluctance (symbol Rm) is the resistance a magnetic path offers to magnetic lines of force () and is measured in ampere turns per weber (At/W).
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 62: 11.5 Magnetisation curves
The way a magnetic material responds to a magnetic field can be shown by measuring the flux density (B) in the material for different values of magnetising force (H).
The magnitude and direction of a magnetic field in a magnetic material can be measured with an instrument called a magnetometer, sometimes known as a Tesla meter, or Gaussmeter.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 63: B–H curve
A B–H curve shows how the flux density changes with
magnetising force
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.27

## Slide 64: Shape of B–H curve
The shape of a B–H curve depends on the material.
Some saturate more rapidly.
Some have a linear region over a wider range of magnetising forces.
Each material will have a different value of flux density at a particular magnetising force.
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.28

## Slide 65: Magnetic hysteresis
A test that yields more information about a magnetic material is achieved by passing an alternating current through the coil.
Because the current is periodically changing direction, the magnetic field will periodically change polarity.
That is, the magnetic core will be magnetised in one direction, then in the other, on a repeating basis.
At no stage is the material saturated.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 66: Hysteresis curve
Called a hysteresis curve (lagging behind) because when H is zero, B is not zero
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.29

## Slide 67: Example hysteresis loops
A ‘soft’ magnetic material is more easily magnetised and
de-magnetised than a ‘hard’ magnetic material
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.30

## Slide 68: Ferrite hysteresis loop
Ferrite is a hard magnetic material with an almost square
hysteresis loop
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.31

## Slide 69: Magnetic losses
1. Hysteresis loss – caused by a material’s hysteresis. A comparison between materials can be seen from their hysteresis curves. The smaller the area enclosed by the curve, the lower the losses.
2. Eddy current loss – which occurs when a coil is supplied with alternating current. To reduce this, the core of the coil is laminated.
3. Fringing and leakage loss – due to flux flowing outside the core.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 70: Reducing eddy current loss
Electromagnets operating with an alternating current have a laminated core to minimise eddy currents flowing in the core
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.32

## Slide 71: Magnetic leakage
Magnetic fringing and leakage contribute to the losses in a
magnetic circuit
Notes: 31 Jul 2026
Install HV equipment
<number>
Figure 11.33

## Slide 72: Summing up
The B–H curve shows how much flux density B is produced in a material at various values of magnetising force H.
Permeability of a magnetic material changes with flux density, and is maximum near the knee of the B–H curve.
A hysteresis loop (or curve) of a magnetic material shows how the flux density changes when the magnetising force is periodically reversed by passing an alternating current through the magnetising coil.
Notes: 31 Jul 2026
Install HV equipment
<number>

## Slide 73: Summing up (2)
The term hysteresis means the lag between the magnetising force and the state of magnetisation of the material.
The smaller the area enclosed by a material’s hysteresis loop, the lower the hysteresis losses in the material, and the more suited the material is for use with an alternating magnetic field.
All magnetic circuits have losses, which include hysteresis loss, eddy current loss, magnetic fringing and leakage.
Notes: 31 Jul 2026
Install HV equipment
<number>