## Slide 1: Chapter Overview
Understanding the TCP/IP protocol suite
Configuring and troubleshooting TCP/IP
Installing, configuring, and troubleshooting NWLink
Understanding and configuring network bindings

## Slide 2: Advantages of Using TCP/IP
A routable networking system supported by most operating systems
The technology for connecting dissimilar systems
A robust, scalable, cross-platform client/server framework
A method of accessing Internet resources

## Slide 3: The TCP/IP Suite of Protocols Maps to a Four-Layer Conceptual Model

## Slide 4: Understanding IP Addresses
Identifies each Transmission Control Protocol/Internet Protocol (TCP/IP) host
Consists of a network ID and a host ID
Consists of a logical 32-bit number (four 8-bit octets)

## Slide 5: Addresses Supported by Microsoft
Class A addresses: 1.0.0.0 through 126.0.0.0
  126 networks and 16,777,214 hosts per network
Class B addresses: 128.0.0.0 through 191.255.0.0
  16,384 networks and 65,534 hosts per network
Class C addresses: 192.0.0.0 through 223.255.255.0
  2,097,152 networks and 254 hosts per network

## Slide 6: Using a Static IP Address

## Slide 7: Obtaining an IP Address Automatically

## Slide 8: Using Automatic Private IP Addressing
Automatically configures Internet Protocol (IP) addresses
  Without using static IP addresses
  Without installing the Dynamic Host Configuration Protocol (DHCP) Service
Provides the ability to create a functioning single-subnet network by default
Does not require a default gateway

## Slide 9: The Automatic Private IP Addressing Process

## Slide 10: The Automatic Private IP Addressing Process for Clients with a Valid Lease at Boot Time
The client tries to renew its lease with the DHCP server.
If the DHCP server is not available, the client pings the default gateway.
  If the default gateway replies, the client continues to use the lease.
  If the default gateway does not reply, the client uses Automatic Private IP Addressing.

## Slide 11: Specifying an Alternate TCP/IP Configuration
If a DHCP server is not found
  You can use an alternate TCP/IP configuration when a computer is used on more than one network and one of the networks does not have a DHCP server and does not use Automatic Private IP Addressing
If you want to disable gateway Automatic Private IP Addressing
  Automatic Private IP Addressing is enabled by default
  If the first TCP/IP configuration fails, Microsoft Windows XP Professional uses the second TCP/IP configuration instead of using Automatic Private IP Addressing

## Slide 12: TCP/IP Tools

## Slide 13: Testing a TCP/IP Configuration

## Slide 14: Introducing NWLink
Is the common name for NWLink IPX/SPX/NetBIOS Compatible Transport protocol (NWLink)
Is Microsoft’s 32-bit implementation of Novell NetWare’s Internetwork Packet Exchange/Sequenced Packet Exchange (IPX/SPX) protocol

## Slide 15: Understanding NWLink Features
Supports communication with NetWare networks
Supports sockets and NetBIOS over IPX
Gives NetWare clients access to applications that run on Microsoft Windows 2000 Server
Requires File and Print Services for NetWare (FPNW) to be installed to give NetWare clients access to file and print resources on Windows 2000 servers

## Slide 16: Installing NWLink

## Slide 17: Configuring NWLink

## Slide 18: Troubleshooting NetWare Connectivity
Tools
  Ipxroute config
  Ipxroute ripout
  Network Monitor
Troubleshooting common NWLink configuration problems
  Verify that NWLink and Client Services for NetWare are installed.
  Verify that Client Services for NetWare is running.
  Verify that the Frame Type is set to AutoDetect on the client.
  Verify the Installed Network Number and Frame Type on the client.

## Slide 19: Introduction to Network Bindings

## Slide 20: Configuring Network Bindings

## Slide 21: Chapter Summary
Microsoft’s implementation of TCP/IP provides a robust, scalable, cross-platform client/server framework that is supported by most large networks.
The TCP/IP suite of protocols maps to a four-layer conceptual model: network interface, Internet, transport, and application.
The four Internet layer protocols—IP, ARP, ICMP, and IGMP—encapsulate packets into Internet datagrams and run all the necessary routing algorithms.
The two transport layer protocols—TCP and UDP—provide communication sessions between hosts.
TCP/IP provides the Winsock and NetBT interfaces for network applications to use the services of the TCP/IP protocol stack.
Each TCP/IP host has a logical IP address that identifies a computer’s location on the network.

## Slide 22: Chapter Summary (Cont.)
Microsoft’s implementation of TCP/IP enables a TCP/IP host to
  Use a static IP address
  Obtain an IP address automatically from a DHCP server
  Use Automatic Private IP Addressing
NWLink provides NetWare clients with access to applications designed for Windows 2000 Server.
To allow a client running Windows XP Professional to access a NetWare server, you must install NWLink and Client Services for NetWare on the client.
Binding allows all bound components to share the services they provide.