## Slide 1: Connect Internal Hardware Components
Ports and Expansion slots

## Slide 2: Ports
A port is a interface on a computer to which you can connect a device. There are output devices like monitors, printers and plotters. Input devices like the keyboard, mouse and scanner. Some PCs come with a serial RS-232C port or 422 port for connecting a modem or mouse and a parallel port for connecting a printer. On PCs, the parallel port uses a 25-pin connector. Small Computer System Interface ports support higher transmission speeds than do some ports and you can attach seven devices to the same port.

## Slide 3: FireWire
The FireWire (IEEE 1394) is a technology of bus that has a bandwidth of 400-1000 Mbps and can handle up to 63 units on the same bus. With fire wire, serial ports are not being used as they had been at the past.
LPT
The Line Printer Terminal is used by some compatible PCs as an identification for the parallel port such as LPT1, 2 or 3. This is required when installing a printer on a PC. All PCs use LPT1 and will not have an option for another port unless more ports are put to the PC.

## Slide 4: PS/2
The PS/2 port (keyboard and mouse) was developed by IBM for connecting a mouse or keyboard to a PC. The port is a mini DIN plug that contains six pins that is found on some compatible PCs today.

## Slide 5: USB
The Universal Serial Bus was introduced in ‘95 by Intel, Compaq, Microsoft just to name some. USB 1.0 is an external bus that supports data transfer rates of 12 Mbps and is capable of supporting up to 127 peripheral devices.
USB 2.0 was also introduced in ‘01 and was developed by HP, Intel, Lucent, Microsoft, NEC and Philips. The hi-speed USB is capable of supporting a transfer rate of up to 480 Mbps and is backwards compatible, meaning it's capable of supporting USB 1.0 and 1.1 devices and cables. With USB, serial ports are not being used as they had at the past.

## Slide 6: USB
SMC-BT10 EZ Connect Wireless Bluetooth USB Adaptor
It allows your PC to work with all Bluetooth devices. Bluetooth technology allows you to communicate with other Bluetooth devices to wirelessly share files, transfer information, print, send and receive email, browse the web and use a mobile phone to access the internet. It supports class 2 Bluetooth and has an operating range of up to 30 feet.

## Slide 7: Expansion slots
A expansion slot is located inside a PC on the motherboard that allows more boards to be connected to it.
AGP
Accelerated Graphics Ports was designed by Intel, August ’97. It’s a port designed for video cards and 3D accelerators. It introduces a point-to-point channel so that the graphics controller can directly access the system memory.
The AGP channel is 32-bits wide and runs at 66 MHz, a total bandwidth of 266 Mbps. It also supports two optional faster modes of 533 Mbps and 1.07 Gbps. And also allows 3-D textures to be stored in main memory rather than video memory.
If the user wants to have more video cards in the PC they would have one AGP video card as well as one or more PCI video cards. Not all operating systems support AGP because of limited or no driver support. Earlier versions of Windows did not add in AGP support.

## Slide 8: EISA
Extended Industry Standard Architecture was developed by IBM in ’88. It’s found on early Pentium PCs. It has an expansion slot which can hold both EISA and 16-bit ISA adaptor cards. The slot on the motherboard is the same length as the 16-bit slot but a single slot. The EISA bus is not usually used or found as the PCI and AGP cards have become the best bus for compatible PCs.
ISA
Industrial Standard Architecture is compatible with different CPU’s. A adaptor for a 25 MHz system years ago will still work in a 600 MHz Pentium PC.

## Slide 9: PCI
Peripheral Component Interconnect was developed by Intel as an expansion to the ISA bus. Some manufacturers make their products with a PCI interface. The specification has room built into it for expansion both in the bus lines and the speed at which these lines can work.
Video Electronics Standards Association
The Video Electronics Standards Association bus uses an extension to the ISA 16-bit slot. The adaptor card has edge connector tabs that fit into the ISA slot also. Some buses run at different speeds.

## Slide 10: OH&S
Electrostatic discharge is what someone can do to damage their PC or hardware components. ESD can occur when working in your PC and will cause components you touch to not work properly. It occurs without the user feeling a shock and will only occur while working on the inside of the PC or handling an expansion card. To prevent ESD use an wrist strap. There are steps to help reduce the chances of ESD:
Turn off the PC.
Zero potential-you can touch the metal side of the PC (case) to earth yourself.
Cords-unplug all cords from the back of the PC, power cord, mouse and keyboard.
Weather-Electrical storms can increase the ESD risk, try not to work on a PC during an electrical storm.
Accessories-it’s also a good idea to remove all jewelry.

## Slide 11: Considerations/requirements
The considerations are to shut down the PC first and turn off the monitor. Turn off the switch and unplug all cables. Wait for the PC to cool before opening the case. To prevent ESD use a wrist strap. The motherboard should be handled with care and place it on a protection anti-static sheet. There’s a minimum system requirement for hardware, and the PC should have ports and expansion slots available in the PC. The requirements are when installing expansion cards into the motherboard, make sure its connected to the correct slot and press it firmly.

## Slide 12: Used devices in G3.32
Expansion slots
4 slots available.
3 PCI-all available.
1 AGP-available.
Data connection slot for ISA-connection slot available for inserting a ISA slot extension kit (allows up to 2 ISA cards to be connected).
Ports
Standard 101/102-key.
PS/2 keyboard and mouse.
USB Root Hub.