## Slide 1: Low Voltage Hazards
Low voltage = Higher than 50V ac, 120Vdc
Lower than High Voltage
Voltage hazards can be reduced by proper system grounding
Step voltage, Touch voltage, Mesh voltage, Transferred voltage

## Slide 2: The nature of hazard
The relationship of frequency to hazard---
Up to 100 HZ--- Similar effect for AC & DC
Above 100 KHZ------- 10 to 100 mA Threshold

## Slide 3: Capacitor discharge
1 micro Farad, 10 KV—Ventricular fibrillation
Specific hazard of electronics equipments
Electric shock from 120 to 240, 480V supply.
Radio frequency
Induced voltage
Non ionizing RF radiation hazard
Electrical Hazard
Chemical Hazard
Explosion Hazard

## Slide 4: Medium and high voltage safety
Open circuit in secondary of current transformers causes high voltage
System grounding --- The connection of one of the conductors to earth.
Reduce the risk to electrocution---
Protective equipments must be used.
Hard hat, Eye protection, Electric arc protection, Rubber glove, Rubber insulated equipments, Voltage testing equipments.

## Slide 5: SAFETY PROCEDURES
Approach distance must be regarded
Qualified person to perform the task
Complete risk analysis
Review and approve the plan and analysis
Documentation & approval procedure
Working by minimizing the risk
PPE– Personal Protection Equipments must be used.

## Slide 6: SAFETY PROCEDURES & METHODS
Think , be aware
Understand your procedure
Follow your procedure
Use appropriate safety equipments
Ask if you are unsure. Do not assume
Do not answer, if you do not really know.

## Slide 7: The steps required before de-energizing
All energy control devices feeding the area must be opened
Lock and tags placed on energy control devices
Voltage measurement
Safety grounding
Qualified inspector inspects the work area
Test the instruments
Measure the equipments being verified
Re-test the instruments.

## Slide 8: ONE MINUTE SAFETY AUDIT
Notify the responsible persons of your presence in area
Listen to any abnormal sounds
Sniff for unusual odours
Locate all fire emergency exits
Locate all fire alarms and telephones
Inspect all transformer insulation liquid levels, temperature and pressure
Locate station one line diagram
Make certain room is neat and tidy

## Slide 9: ONE MINUTE SAFETY AUDIT
Be certain that all required equipments are readily available and easily reached
Check to see that all protective relays and other operational flags are properly reset
ELECTRICAL INSTALLATION SAFETY
Proper design
Selection
Installation
Calibration

## Slide 10: ENGINEERING
Property testing
Physical setting of devices
To certain that the equipment is capable of performing when called upon.

## Slide 11: HUMAN FACTORS IN ELECTRICAL SAFETY
Sense physical stimuli
Perceive and process information
Act

## Slide 12: SLOW REACTION
Sleep deprivation
Fatigue
Time of delay
Environmental extreme
Alcohol
Drug use
Medical problem
Nutrition